700001

TEMPOMIX 2 time flow mixer

Артикул: 700001

Технические характеристики

Deck-mounted time flow basin mixer:

Time flow ~7 seconds.

Flow rate pre-set at 3 lpm at 3 bar, can be adjusted from 1.5 - 6 lpm.

Tamperproof, scale-resistant flow straightener.

Chrome-plated solid brass body.

PEX flexibles with stopcocks F3/8", filters and non-return valves.

Fixing reinforced by 2 stainless steel rods.

Side temperature control with standard lever and adjustable maximum temperature limiter.

AB anti-blocking system: water only flows when push-button is released.

10-year warranty.