792310

SECURITHERM shower panel

Артикул: 792310

Технические характеристики

Thermostatic time flow shower panel:

Aluminium epoxy-coated shower panel for wall-mouted, exposed installation.

Concealed inlet via flexibles M1/2".

SECURITHERM thermostatic mixer.

Adjustable temperature control from cold water up to 38°C with 1st limiter set at 38°C and 2nd limiter set at 41°C.

Anti-scalding safety: immediate shut-off if cold water supply fails.

Thermal shocks are possible.

Time flow ~30 seconds, soft-touch operation.

Flow rate set at 6 lpm at 3 bar.

Chrome-plated, tamperproof ROUND shower head with scale-resistant nozzle and automatic flow rate regulation.

Concealed fixings.

Filters and non-return valves.

10-year warranty.